|  | Plywood Plant |  |
| --- | --- | --- |
|  | Major supplier | RAUTE |  |
|  | Year of manufacturing | 1999 |  |
|  | Press type | 20 openings |  |
|  | Platen size |  | mm |
|  | Max panel sizes | 1.650 x 2.600 | mm |
|  | Scope of supply |  |  |
|  | Log Saw, make | HAWA, type H 254/1600/KS/H |  |
|  | Max. log diameter | 1.000 | mm |
|  | Cutting blade length | 1.850 | mm |
|  | Log debarker with movable milling body, make | RAUTE |  |
|  | Peeling line | RAUTE, 800 x 2700 |  |
|  | Log length | 1.320, 1.900, 2.650 | mm |
|  | Log diameter | 200-800 | mm |
|  | Veneer thickness | 1,1-3,5 | mm |
|  | Voltage | 380/220/50 | V/Hz |
|  | Capacity, approx. | 8.0 | m3/h |
|  | Rotary Clipper |  |  |
|  | Accuracy at 200 m/min speed | +/-5 | mm |
|  | Clipping speed adjustable to wood species |  |  |
|  | Knife replacement time | 15 min. |  |
|  | Knife sharpening interval, approx. | 2 | weeks |
|  | Veneer Dryer | RAUTE, Roller type |  |
|  | No. of decks | 4 | pieces |
|  | Roller length | 4.800 | mm |
|  | Heating medium | Thermal oil |  |
|  | Stack infeed conveyor, type | PSKY 2800/1400 |  |
|  | Conveyor speed | 0,2 | m/s |
|  | Max. load /1 meter chain | 1.000 | Kg/m |
|  | Length | 5.400 | mm |
|  | Width | 2.100 | mm |
|  | Delivery capacity | 13 | m3/h |
|  | Lifting platform |  |  |
|  | Lifting height | 1.350 | mm |
|  | Lifting time, min. | 50 | sec |
|  | Delivery capacity | 16 | m3/h |
|  | Veneer feeder |  |  |
|  | Length of speed-up roller | 4.800 | mm |
|  | Speed | 3,5 | m/s |
|  | Length | 1.100 | mm |
|  | Width | 5.700 | mm |
|  | Delivery capacity | 24 | m3/h |
|  | Gluing machine, type | RAUTE, LEY 2700 |  |
|  | Roller length | 2.700 | mm |
|  | Diameter of contact rollers | 300 | mm |
|  | Diameter of dosing rollers | 230 | mm |
|  | Speed | 63 | m/min |
|  | Machine length | 4.600 | mm |
|  | Machine width | 1.250 | mm |
|  | Roller height | 1.680 | mm |
|  | Pre-press | RAUTE |  |
|  | Platen sizes | 1.750 x 2.700 | mm |
|  | Max. opening | 1.300 | mm |
|  | Max. sizes | 1.650 x 2.600 | mm |
|  | Min. sizes | 1.000 x 1.600 | mm |
|  | Max. stack height | 1.300 | mm |
|  | Hot press | RAUTE |  |
|  | No. of openings | 20 |  |
|  | Platen sizes | 1.750 x 2.700 | mm |
|  | Max. board sizes | 1.650 x 2.600 | mm |
|  | Max. spec. pressure | 20 | bar |
|  | Heating medium | Thermal oil |  |
|  | Trimming machine | HOLZMA |  |
|  | Panel size max | 2.200 x 3.800 | mm |
|  | Panel size min | 1.000 x 2.000 | mm |
|  | Saw blade projection | 110 | mm |
|  | Cutting length – rip saw | 3.800 | mm |
|  | Cutting length – cross cut saw | 2.200 | mm |
|  | Sanding machine | STEINEMANN Osus Novella 160/4 | K-NS-MC |
|  | Sanding heads | 4 |  |
|  | Max working width | 1.600 | mm |
|  | Production speed | 18 | m/min |
|  | Board thickness | 3-30 | mm |
|  | Board width | 1.560 | mm |
|  | Board length | 2.500 | mm |
|  | Removal | 0.5-1 | mm |
|  | Veneer Jointing machine | FISCHER RUCKLE, EFA 28 |  |
|  | Veneer strip length | 420 – 2.780 | mm |
|  | Veneer-strip thickness | 0.8 – 6 | mm |
|  | Veneer-strip width (glued) | 60 – 800 | mm |